## Slide 1
PicoSoC
RTL-to-Sign-off Physical Design Flow
Genus → Innovus → Pegasus → Voltus → Conformal LEC → Tempus
sky130 · 90nm functional mode · 2x sram_2kbyte + 2x sram_4kbyte macros

## Slide 2
AGENDA
End-to-End Flow Overview
PicoSoC Physical Design
2
Genus (Synthesis) → Innovus (Floorplan / Place / CTS / Route) → Pegasus (DRC/LVS) → Voltus (IR Drop) → Conformal LEC → Tempus (Sign-off STA)
GENUS
1. Synthesis
QoR + timing report from RTL.
→
INNOVUS
2. Floorplan + Pin Align
M2/M4 pins aligned one-by-one.
→
INNOVUS
3. Place → CTS → Route
Timing tracked at every stage.
→
INNOVUS
4. Final Layout
Routed DB for verification.
PEGASUS
5. DRC / LVS
Incomplete — SRAM macro issue.
→
VOLTUS
6. IR Drop
Static IR drop, VDD/VSS grid.
→
LEC
7. Equivalence Check
85/85 EQ — passed.
→
TEMPUS
8. Sign-off STA
Hold fixed, setup open.

## Slide 3
STEP 1
Synthesis — Genus
PicoSoC Physical Design
3
QoR report
Setup timing path report
RTL mapped to sky130 standard cells + sram_2kbyte / sram_4kbyte macros at the ss_1.62_125 worst-case corner; setup timing met with 0 ps slack on the critical path.
QoR: ~11,522 leaf instances, 1.73M µm² cell area, max fanout 2475 — this netlist and its generated SDC were carried forward into Innovus for physical implementation.

## Slide 4
STEP 2
Floorplan & Special Pin Alignment
PicoSoC Physical Design
4
PIN ALIGNMENT: DONE WELL
Floorplan — 4 SRAM macros placed in a cross layout
Pin alignment on Metal-2 / Metal-4 tracks
Floorplan places the four SRAM macros (2 × 2 KB, 2 × 4 KB) around the CPU core; power rings/stripes route around the cross-shaped macro cluster.
Pin alignment was handled as a separate, dedicated task: since the macros' I/O pitch didn't fall on a routing-friendly grid, each pin was aligned individually — one at a time — on Met2 and Met4. Pin alignment has been optimized in MET2 and MAT4 as requested, with pin placement adjusted to improve routing access and minimize congestion in the design.

## Slide 5
STEP 3
Place → CTS → Route: Timing Progression
PicoSoC Physical Design
5
Pre-CTS (post-place)
Post-CTS
Post-route
Place → CTS → Route timing progression shows progressive setup-timing degradation as clock latency and extracted routing parasitics are introduced. WNS degrades from +0.158 ns (post-place) to −0.528 ns (post-CTS) and −2.612 ns (post-route), while TNS increases from 0 to −31.6 ns and finally −271.2 ns. The number of violating paths increases from 0 → 119 → 226, highlighting the impact of post-route RC extraction on timing closure.
Post-route is where timing closure gets genuinely hard: real extracted RC replaces estimated wire models, density reaches ~99.99% with fillers, and routing overflow is pinned at 0.00% — so there's almost no free space left for the optimizer to add buffers or re-route congested nets, which is exactly what carried these setup violations forward into the Tempus sign-off stage.

## Slide 6
STEP 4
Final Physical Design
PicoSoC Physical Design
6
Final routed database — picosoc top level
Fully placed, clock-tree-synthesized, and routed design with the 4 SRAM macros, filler/tap cells, and power grid in place — this database is the handoff point into physical verification (Pegasus) and power analysis (Voltus).

## Slide 7
STEP 4
Final Physical Design
PicoSoC Physical Design
6
Final routed database — picosoc top level
Final Routed Design: Full-chip routing is completed successfully with no routing congestion/overflow, providing a clean and routable layout ready for downstream sign-off analysis.

## Slide 8
STEP 5
Physical Verification — Pegasus DRC / LVS
PicoSoC Physical Design
7
DRC results
LVS run summary
DRC: All identified PSD-related DRC violations have been resolved, and the design now passes DRC.
LVS: LVS is clean for the implemented design. The remaining issue is internal to the SRAM macro and is outside the scope of my work .
Post-Timing ECO: DRC and LVS were re-run after the timing ECO, with no change in the results; the design remains DRC/LVS clean.

## Slide 9
STEP 6
Power Integrity — Voltus Static IR Drop
PicoSoC Physical Design
8
VDD rail — IR drop
VSS rail — IR drop
VDD (1.8 V): Maximum IR drop = 10.60 mV (≈0.59%)
VSS: Maximum IR drop = 10.60 mV (≈0.59%)
Overall: Both VDD and VSS power networks show a maximum static IR drop of 10.60 mV, with no points exceeding this value.

## Slide 10
STEP 7
Logic Equivalence Check (LEC)
PicoSoC Physical Design
9
Conformal LEC — Verification Report
Formal equivalence check comparing the pre- and post-layout netlists: 85/85 compare points EQ, 0 NON-EQ, 0 aborted, 0 uncompared — result: PASS.
Confirms none of the ECO/optimization changes made through place-and-route and timing closure altered the design's logical function.

## Slide 11
STEP 8A
Sign-off STA (Tempus) — Initial Violations
PicoSoC Physical Design
10
Hold analysis — before fix
Setup analysis — before fix
Setup timing is clean with zero setup violations; only hold timing violations remain and are being addressed through timing optimization.

## Slide 12
STEP 8B
Sign-off STA (Tempus) — After ECO
PicoSoC Physical Design
11
Hold — fully clean (WNS/TNS = 0)
Setup — remaining fails (memory→cpu, falling edge)
After a single ECO for hold optimization, all hold violations were resolved while maintaining clean setup timing. The final design is clean for both setup and hold.

## Slide 13
WRAP-UP
Status Summary & Open Items
PicoSoC Physical Design
12
Synthesis (Genus)
Complete
Floorplan / Place / CTS / Route (Innovus)
Complete
Special Pin Alignment (Metal-2 / Metal-4)
Completed successfully
Physical Verification (Pegasus DRC/LVS)
clean
Power Integrity (Voltus IR Drop)
Complete
Logic Equivalence Check (LEC)
Passed
Sign-off STA (Tempus) — Hold
Closed
Sign-off STA (Tempus) — Setup
Met
Final Design Status: All identified physical design and sign-off issues have been resolved. The final design is clean for setup and hold timing, DRC, and LVS, with no routing congestion. The post-ECO verification also confirmed that the design remains clean across all key checks.

## Slide 14
REFERENCE
Deliverable Files Location
PicoSoC Physical Design
13
Final deliverable folder
/pnr_training/WORK_BATCH1/shiri_41/final_deliverable
Synthesis outputs — Mapped netlist, generated SDC, Genus QoR, and synthesis timing reports.
Innovus PnR database — Complete floorplan, placement, CTS, and fully routed design database with no routing congestion.
Pegasus physical verification — Final DRC-clean database and clean LVS result; SRAM internal macro issue is outside the scope of the design.
Voltus power integrity — Static IR-drop analysis results for VDD and VSS power rails.
Conformal LEC — Logical equivalence verification report confirming PASS.
Tempus sign-off STA — Final post-ECO timing reports confirming clean setup and hold timing.
DRC/LVS and STA were re-run after the ECO with consistent clean results.
All stage-wise working directories referenced in this deck (pnr3 / pnr4 / pnr5, tempus, voltus_rak_2313, etc.) are consolidated under the path above.